## Slide 1: System Center, PowerShell and 802.1X NAC
Christian Lehrer @chri_tea
Connecting the dots for easy device integration

## Slide 2: Agenda
802.1X
  Overview
  Benefits
  Shortcomings
  MAC-Bypass
Automated device registration
  Demo
  Process description

## Slide 3: IEEE* 802.1X – Overview
Supplicant
Authenticator
Authentication Server
RADIUS
1.
2.
3.
4.
Company network
with Computer
Certificate
* Institute of Electrical and Electronics Engineers
Notes: IEEE Standard for port-based Network Access Control. Das Institute of Electrical and Electronics Engineers
Often implemented in Wireless LANs
Good for Domain-Environments with existing PKI

## Slide 4: Benefits of 802.1X
The VLAN is based on supplicant – the RADIUS defines the VLAN for the port while supplicant is connected
Knowledge – Which devices are connected to the company network and where
Secure network ports in meeting rooms etc.

## Slide 5: Shortcomings of 802.1X Cert-based
Devices that can not handle certificates can not be authenticated.
  Old devices
  Line of business devices
  Mulifunction printers
  IP-phones

## Slide 6: 802.1X MAC-Bypass
For those devices the „MAC-Bypass“ implementation can be used.
A known device can be registered with MAC-adress in the RADIUS and thus be authenticated.
Contra MAC-Bypass:
busy hepldesk and thus slow process for users

## Slide 7: 802.1X automated device registration
End User Self service portal
Orchestrator & PowerShell
ARUBA Clearpass API
Automated device registration
+
+
=

## Slide 8: Demo
$Audience = Get-Audience
If ($Audience.status –eq ‘nearly asleep‘) {
Set-Audience –Status awake –Force }

## Slide 9
# Video Self Service Portal ServiceManager.mp4
# Video Orchestrator Orchestrator_reviewed.mp4
# PowerShell script to create XML CreateNACDevices.xml
# Video ARUBA Clearpass Aruba_reviewed.mp4

## Slide 10: Summary
802.1X can be implemented in a way users can accept it.
User self service portals are important for your automation success.
APIs are your friends.

## Slide 11: Next Steps...
Now: 15 min break
Grab a coffee
Stay here to enjoy next presentation
Change track and switch to another room
Ask me questions or meet me in a breakout session room afterwards

## Slide 12: Questions?

## Slide 13: About_Author
Christian Lehrer
System Architect at Diehl Controls
Twitter.com/chri_tea
www.christianlehrer.com
PowerShell Usergroup Southern Germany
www.powershell-ug.com